## Slide 1: A compact injection-locked UV laser system for quantum information processing
Nikolay Videnov
Quantum Information with Trapped Ions (QITI) Group

## Slide 2: UV lasers
Uses
  Micro lithography
  Laser ablation
  Trapped ions
Getting UV light
  Frequency doubling Ti:sapph
  ECDL laser
  Injection locking

## Slide 3: Injection Locking
Cavity laser
  Gain medium electronically pumped
  Saturation occurs forcing lasing
Injection locking
  Inject seed signal
  Above threshold power is diverted into injected singal

## Slide 4: Physically realizing Injection Locking
Need a few mW from a seed laser
Faraday isolator
Slave laser diode
T. Hosoya et al., Review of Scientific Instruments 86, 2015

## Slide 5: Diode Selection
Locking only happens around the free running oscillation frequency of the diode.
Need a laser diode around 369nm
The closest commercially available diode can be frequency selected to ~371nm*
  Cool to 369nm?
*Nichia NDU4116 (370-380nm)

## Slide 6: Cooling Laser Diode
40°C below lab temperature
  Achievable with Thermoelectric Coolers (Peltier elements)
  A few heat load calculations later we pick a pair of TECs

## Slide 8: Laser Enclosure
Pressurize with dry nitrogen
Feedthroughs
  Optical
  Pressurized air
  electrical

## Slide 10: Laser Enclosure
Machined the design
Time to test!

## Slide 11: Climate Measurement
There’s a leak!
Make a blank and seal the D-sub connector

## Slide 12: A fix all solution
5 minute epoxy
A measurable improvement!

## Slide 13: Putting it all together
Machined diode holder and enclosure
Compact collimation
Water-cooling
Constant current controller

## Slide 14: Experimental setup

## Slide 15: Results
Same slope from the datasheet
Effective cooling
Proof of concept

## Slide 16: Conclusion/Outlook
Injection locking is an excellent way to amplify laser power
The challenges of injection locking can be tackled effectively with this design

## Slide 17
Quantum Information with Trapped Ions (QITI)
research.iqc.uwaterloo.ca/qiti/
Roland Hablützel
Chung-You (Gilbert) Shih
Nikhil Kotibhaskar
Sainath Motlakunta
G R A D U A T E S T U D E N T S
U N D E R G R A D U A T E S
P O S T D O C S
Fereshteh Rajabi
Yi Hong
Teoh

## Slide 18: Injection Locking