## Slide 1: A compact injection-locked UV laser system for quantum information processing
Nikolay Videnov
Quantum Information with Trapped Ions (QITI) Group

## Slide 2: Quantum Information With Trapped Ions
New lab
Quantum simulator using trapped ions
Tackle computationally hard problems using an engineered Hamiltonian
See me after talk if you’re interested!

## Slide 3: UV lasers
Uses
  Laser Cooling
  Optical pumping
  State Detection
Getting UV light
  Frequency doubling Ti:Sapph
  External Cavity Diode Laser
  Injection locking
Dr. Lindsay LeBlanc, keynote presentation, CUPC 2018

## Slide 4: Cavity Laser
Non linear gain medium
  Broadly amplifies
  Finite gain at saturation
Feedback
  Filters out higher order modes
  Allows buildup of power in single mode

## Slide 5: Injection Locking
Replace feedback with signal from master laser
Need a threshold amount of power to overtake the natural mode
Narrow locking range
Lasers, A E Siegman, 1986

## Slide 6: Physically realizing Injection Locking
Need ~100µW from a master laser
Faraday rotator
Slave laser diode
Generic optics
T. Hosoya et al., Review of Scientific Instruments 86, 2015

## Slide 7: Diode Selection
Locking only happens around the free running oscillation frequency of the diode.
Need a laser diode around 369nm
The closest commercially available diode can be frequency selected to ~371nm*
  Cool to 369nm?
*Nichia NDU4116 (370-380nm)

## Slide 8: Test Fixture
40°C below lab temperature
  Achievable with Thermoelectric Coolers (TEC)
A few heat load calculations later we pick a pair of TECs
  Make a test block
  Add a dummy load
Cool to desired temperature
Dummy load
Test diode holder

## Slide 9: Laser Enclosure
Cooling below the dew point causes
  Condensation
  frost
Pressurize with dry nitrogen
Feedthroughs
  Optical
  Pressurized air
  electrical
Dummy load
Test diode holder
TEC
Water Cooling
block
Water Cooling
block
TEC
Frost

## Slide 11: Laser Enclosure
Machined all the parts in the CAD model
Pressurize and cool
¼” NPT ball valve
O-ring
Water cooling
bock
Diode Holder
D-sub connector
Pressure Sensor

## Slide 12: Pressure Measurement
There’s a leak!
Make a blank and seal off the electrical feedthrough

## Slide 13: A fix all solution
5 minute epoxy
A measurable improvement!

## Slide 14: Putting it all together
Machined diode holder and enclosure
Compact collimation
Water-cooling
Constant current controller

## Slide 15: Experimental setup

## Slide 16: Results
Cooled diode without condensation
Achieved a 1.5nm frequency shift
  Sufficient to bring diode to injection locking range
Slope matches datasheet

## Slide 17: Conclusion/Outlook
Injection locking is an excellent way to amplify laser power
The challenges of diode cooling can be compactly solved with this design
Future work
  Optics setup
  Swapping blue ray diode to Nichia diode

## Slide 18
Quantum Information with Trapped Ions (QITI)
research.iqc.uwaterloo.ca/qiti/
Chung-You (Gilbert) Shih
Nikhil Kotibhaskar
Sainath Motlakunta
G R A D U A T E S T U D E N T S
Roland Hablützel
P O S T D O C S
Fereshteh Rajabi
U N D E R G R A D S
Yi Hong
Teoh
Rajibul
Islam
P I

## Slide 19: Peltier cooling (TEC)
NP junctions used to move heat from one side to other side
In a thermocouple a temperature difference at the junction of dissimilar materials produces a voltage
TEC cooling is a thermocouple in reverse

## Slide 20: Injection Locking

## Slide 23: Head Load